## Slide 1
Identify the contactors:
set the typedefed enumerationCONT_NAMES_e, e.g
typedef enum {
CONT_PLUS_MAIN = 0,
CONT_PLUS_MAIN_PRECHARGE = 1,
CONT_MINUS_MAIN = 2,
} CONT_NAMES_e;
Define names of the contactors
physical pins (given in the io_mcu_cfg.h) , e.g.
PIN_MCU_0_CONTACTOR_0_CONTROL
mapped to (defined) meaningful names, e.g.
CONT_PLUS_MAIN_PRECHARGE_CONTROL
Results in
#define CONT_PLUS_MAIN_CONTROL PIN_MCU_0_CONTACTOR_1_CONTROL
contactor_cfg.h
Configuration of the contactor:
CONT_CONFIG_s cont_contactors_config [] = {
{CONT_PLUS_MAIN_CONTROL, CONT_PLUS_MAIN_FEEDBACK,
CONT_FEEDBACK_NORMALLY_OPEN}
};
contactor_cfg.c
state of contactor
{ 0, CONT_SWITCH_OFF},
set value
measured feedback
typedefed states of the contactors CONT_SWITCH_e
typedef enum {
CONT_SWITCH_OFF = 0,
CONT_SWITCH_ON = 1,
CONT_SWITCH_UNDEF = 2,
} CONT_SWITCH_e;
typedefed feedback type
CONT_FEEDBACK_TYPE_e
typedef enum {
CONT_FEEDBACK_NORMALLY_OPEN = 0,
CONT_FEEDBACK_NORMALLY_CLOSED = 1,
CONT_HAS_NO_FEEDBACK = 0xFF
} CONT_FEEDBACK_TYPE_e;